Top of Form MSDS Database Search Resource Site Bottom of Form Material Safety Data Sheet Name SUNISO 3GS REFRIGERATION OIL MSDS ckcld Company VIRGINIA K M P CORP FSC 9150 MSDS Safety Information FSC: 9150 NIIN: 00-664-4449 MSDS Date: 04/26/1999 MSDS Num: CKCLD Product ID: SUNISO 3GS REFRIGERATION OIL MFN: 01 Responsible Party Cage: 8J132 Name: VIRGINIA K M P CORP Address: 4100 PLATINUM WAY City: DALLAS TX 75237 Info Phone Number: 214-330-7731 Emergency Phone Number: 214-330-7731 Resp. Party Other MSDS No.: CAT. NO.: L316, L318, L321, L324 Preparer's Name: VIRGINIA KMP CORP Chemtrec IND/Phone: (800)424-9300 Review Ind: Y Published: Y Contractor Summary Cage: 8J132 Name: VIRGINIA K M P CORPORATION Address: 4100 PLATINUM WAY City: DALLAS TX 75237 Phone: 214-330-7731 Item Description Information Item Manager: S9G Item Name: LUBRICATING OIL,REFRIGERANT COMPRESSOR Specification Number: VV-L-825 Unit of Issue: GL UI Container Qty: 6 Type of Container: CAN Ingredients Cas: 64742-52-5 RTECS #: PY8035000 Name: MINERAL OIL Health Hazards Data LD50 LC50 Mixture: LD50: 402 G/KG (SKIN:MOUSE) MINERAL OIL Route Of Entry Inds - Inhalation: YES Skin: NO Ingestion: NO Carcinogenicity Inds - NTP: NO IARC: NO OSHA: NO Effects of Exposure: INHALATION: HARMFUL IF INHALED, BUT UNLIKELY IN NORMAL USE. EYE: EYE IRRITATION DEVELOPS IMMEDIATELY UPON CONTACT. SKIN: CAUSES SKIN IRRITATION; MAY AGGRAVATE PRE-EXISTING SKIN DISORDERS. INGESTION: I RRITATES GASTROINTESTINAL TRACT. CHRONIC EFFECTS: NONE ESTABLISHED. Explanation Of Carcinogenicity: NONE LISTED. Signs And Symptions Of Overexposure: NONE PROVIDED BY MFR. Medical Cond Aggravated By Exposure: NONE PROVIDED BY MFR. First Aid: INHALATION: REMOVE VICTIM TO FRESH AIR AND, IF NEEDED, IMMEDIATELY BEGIN ARTIFICIAL RESPIRATION. GIVE OXYGEN IF BREATHING IS LABORED. GET EMRGENCY MEDICAL HELP. CONTACT A PHYSICIAN IMMEDIATELY. EYE: F LUSH EYES WITH WATER FOR 15 MINS. GET MEDICAL ATTENTION IF SYMPTOMS DEVELOP ANDamp; PERSIST. SKIN: FLUSH WITH WATER OR SOAP ANDamp; WATER FOR 15 MINS. OR UNTIL TRACES HAVE BEEN REMOVED. SEEK MEDICAL ATTENTION IF SYMPTOMS DEVELOP ANDamp; PERSIST. INGESTION: DO NOT INDUCE VOMITING. RINSE MOUTH OUT WITH WATER. GET IMMEDIATE MEDICAL ATTENTION. Handling and Disposal Spill Release Procedures: CLEAN UP LEAKS/SPILLS IMMEDIATELY TO PREVENT SOIL OR WATER CONTAMINATION. WATER SPILL: FLOATING WATER HAZARD. COLLECT ANDamp; PLACE IN CHEMICAL WASTE CONTAINER. NOTIFY APPROPRIATE AUTHORITIES. LAND SPILL: E MERGENCY RESPONSE COORDINATOR MUST HAVE MANDATED TRAINING. ELIMINATE ALL IGNITION SOURCES. SM SPILLS: PICK UP WITH ABSORBENT MATERIALS ANDamp; PLACE IN NON-LEAKING CONTAINERS; SEAL TIGHTLY FOR PROPER DISPO Neutralizing Agent: NONE PROVIDED BY MFR. Waste Disposal Methods: DISPOSE AS HAZARDOUS WASTE. CLASSIFICATION ANDamp; DOCUMENTATION IS REQUIRED BEFORE DISPOSAL. FOLLOW ALL LOCAL, STATE, ANDamp; FEDERAL REGULATIONS. Handling And Storage Precautions: HANDLING: AFTER HANDLING THIS PRODUCT, WASH HANDS BEFORE EATING, DRINKING, OR SMOKING. AVOID CONTACT WITH SKIN, EYES, ANDamp; CLOTHING. IF CONTACT OCCURS, REMOVE CONTAMINATED CLOTHING. IF NEEDED, TAKE FIRST AID ACTION. LAUNDER CONTAMINATED CLOTHING BEFORE REUSE. STORAGE: STORE AWAY FROM OXIDIZERS ANDamp; SOURCE Other Precautions: NONE PROVIDED BY MFR. Fire and Explosion Hazard Information Flash Point: =150.C, 302.F Autoignition Temp Text: N/D Lower Limits: NOT DETERMIN Upper Limits: NOT DETERMIN Extinguishing Media: DRY POWDER, CARBON DIOXIDE (CO2), WATER FOG OR SPRAY. Fire Fighting Procedures: KEEP UNNECESSARY PEOPLE AWAY; ISOLATE AREA. FIREFIGHTERS SHOULD WEAR NIOSH ARRPOVED SELF CONTAINED BREATHING APPARATUS. APPROACH FIRE FROM UPWIND SIDE. AVOID BREATHING SMOKE, FUMES, MIST, OR VAPORS ON THE DOWNWIND SIDE. Unusual Fire/Explosion Hazard: COMBUSTABLE LIQUID, ACID SMOKE AND IRRITATING FUMES. Control Measures Respiratory Protection: NONE PROVIDED BY MFR. Ventilation: LOCAL EXHAUST VENTILATION RECOMMENDED Protective Gloves: USE GLOVES TO PREVENT PROLONGED SKIN CONTACT Eye Protection: NONE PROVIDED BY MFR. Other Protective Equipment: NONE PROVIDED BY MFR. Work Hygienic Practices: WASH HANDS BEFORE EATING, DRINKING, OR SMOKING. REMOVE CONTAMINATED CLOTHING. LAUNDER CONTAMINATED CLOTHING BEFORE REUSE. Supplemental Safety and Health: NONE PROVIDED BY MFR. Physical/Chemical Properties HCC: N1 Boiling Point: =260.C, 500.F M.P/F.P Text: NOT PROVIDED Decomp Text: NOT PROVIDED Vapor Pres: NEGLIGIBLE Vapor Density: ANDgt;5 (AIR=1) Spec Gravity: 0.9 Viscosity: NOT PROVIDED Evaporation Rate ANDamp; Reference: gt;1 (N-BUTYL ACETATE=1) Solubility in Water: INSOLUBLE Appearance and Odor: LIGHT GOLDEN LIQUID, OIL ODOR Reactivity Data Stability Indicator: YES Stability Condition To Avoid: IGNITION SOURCES Materials To Avoid: OXIDIZERS Hazardous Decomposition Products: COMBUSTION: SMOKE, CARBON MONOXIDE, CARBON DIOXIDE Hazardous Polymerization Indicator: NO Conditions To Avoid Polymerization: WILL NOT OCCUR Toxicological Information Transportation Information Responsible Party Cage: 8J132 Trans ID NO: 151597 Product ID: SUNISO 3GS REFRIGERATION OIL MSDS Prepared Date: 04/26/1999 Review Date: 02/21/2000 MFN: 1 Net Unit Weight: 1 GAL Multiple KIT Number: 0 Unit Of Issue: GL Container QTY: 6 Type Of Container: CAN Detail DOT Information DOT PSN Code: ZZZ DOT Proper Shipping Name: NOT REGULATED BY THIS MODE OF TRANSPORTATION Detail IMO Information IMO PSN Code: ZZZ IMO Proper Shipping Name: NOT REGULATED FOR THIS MODE OF TRANSPORTATION Detail IATA Information IATA PSN Code: ZZZ IATA Proper Shipping Name: NOT REGULATED BY THIS MODE OF TRANSPORTATION Detail AFI Information AFI PSN Code: ZZZ AFI Proper Shipping Name: NOT REGULATED BY THIS MODE OF TRANSPORTATION HAZCOM Label Product ID: SUNISO 3GS REFRIGERATION OIL Cage: 8J132 Company Name: VIRGINIA K M P CORPORATION Street: 4100 PLATINUM WAY City: DALLAS TX Zipcode: 75237 Health Emergency Phone: 214-330-7731 Label Required IND: Y Date Of Label Review: 02/21/2000 Status Code: A Origination Code: F Signal Word: CAUTION Health Hazard: Slight Contact Hazard: Slight Fire Hazard: None Reactivity Hazard: None Hazard And Precautions: INHALATION: HARMFUL IF INHALED, BUT UNLIKELY IN NORMAL USE. EYE: EYE IRRITATION DEVELOPS IMMEDIATELY UPON CONTACT. SKIN: CAUSES SKIN IRRITATION; MAY AGGRAVATE PRE-EXISTING SKIN DISORDERS. INGESTION: I RRITATES GASTROINTESTINAL TRACT. CHRONIC EFFECTS: NONE ESTABLISHED. Disclaimer (provided with this information by the compiling agencies): This information is formulated for use by elements of the Department of Defense. The United States of America in no manner whatsoever expressly or implied warrants, states, or intends said information to have any application, use or viability by or to any person or persons outside the Department of Defense nor any person or persons contracting with any instrumentality of the United States of America and disclaims all liability for such use. Any person utilizing this instruction who is not a military or civilian employee of the United States of America should seek competent professional advice to verify and assume responsibility for the suitability of this information to their particular situation regardless of similarity to a corresponding Department of Defense or other government situation.